## Slide 1: Autonomous Helicopter Navigation System 2010

## Slide 2: Contents

## Slide 3: Introduction to AHNS 2010

## Slide 4: AHNS Project Aim
AHNS: To develop an autonomous indoor helicopter navigation system capable of carrying a payload.

## Slide 5: Ground Control Station & Flight control
Tim Molloy

## Slide 6: Role of the GCS and Control
HLO-4 Autonomous Hovering Flight
An autopilot system should be developed to enable sustained indoor autonomous hovering flight. The control system should be designed to enable future ingress and egress manoeuvre to longitudinal and hovering flight.
HLO-5 Ground Control Station
A ground control station that supports appropriate command and system setting inputs and data display and logging should be developed. The design should be derived from previous AHNS developments and enable future ground station developments.

## Slide 7: Software Architecture

## Slide 8: Ground Control Station
HLO-5 Ground Control Station
SR-B-09 and 08 Receive and Transmit Telemetry via WLAN
SR-D-08 Log Telemetry and Uplink Commands
SR-D-09 Display of State and Control Data
SR-D-10 System Status Display
Received Console and Data Logger
Data Plotters & Artificial Horizon
System Status
WiFi Communications
SR-B-02 Flight Mode Switching
Not Yet Implemented

## Slide 9: Ground Control Station
Ubuntu 32-bit Operating System
Qt Framework for C++ GUI Development
Focus on:
  Code reuse
    Creating and using reusable code
  User layout customisation
    Avoid Static GUI objects
      Dockable Widgets
    Enable the operator to choose a layout logical to their application
    Increases the information which can be displayed

## Slide 10: The Widgets
WiFi Communications
  Configure, Control and Monitor UDP Telemetry
Received Console
  Report telemetry messages and enable inspection
System Status
  Provide visual notifications of airborne system status
Data Logger
  CSV Log of all Received Airborne Data

## Slide 11: Data Plotters & Artificial Horizon
Artificial Horizon
  2009 OpenGL Attitude Display
  Roll and Pitch
Data Plotter
  Real-time data plotting
  Raw Sensor Data, State Data, Control Data, System Status…
  Support for multiple data plotters

## Slide 12: Following Controller Design…
Attitude Control Trims and Bounds
  Set the trims and bounds on the roll, pitch and yaw control loops.
Attitude Control Gains
  Set the PID control gains on the roll, pitch and yaw control loops.
Guidance Control Gains
  Set the PID control gains on the x, y and z position control loops.
Guidance Trims and Bounds
  Set the trims and bounds of the x, y and z position control loops.
Flight Control
  Set the active control loops and their set points. Enables command of the airborne control.

## Slide 13: Flight Control
HLO-4 Autonomous Hovering Flight
SR-B-03 50Hz Control Rate
SR-B-10 PID Control Methodology
SR-D-03 Stability Augmented Flight
SR-D-04 Autonomous Station-keeping
Flight Computer
Quadrotor Control
Attitude Control
Guidance

## Slide 14: Flight Computer
Trade Study for Computer-on-Module to support
  Hardware Integration
  Control and State Estimation
  Localization
Considered
  BeagleBoard
    Limited Hardware Interfacing
  Gumstix Overo Air
    Lacked Support for Image Processing
  Gumstix Verdex
    No Hardware Floating Point Implementation
  Gumstix Overo Fire
    6 grams, 600MHz TI CPU

## Slide 15: Quadrotor Control
Thrust Altitude Control Forces
Thrust Roll Control Forces
Thrust Pitch Control Forces
Drag Yaw Control Forces
Motor Output Signals

## Slide 16: Attitude Control

## Slide 17: Guidance